## Slide 1: Fiber Diffraction of Muscle

## Slide 2: Why X-ray Diffraction of Muscle?
2
Force producing events occur on the time scale of ≤ 1 ms
Relevant size scale is 5 - 50 nm for molecular machinery
X-ray diffraction only technique that allows simultaneous collection of structural and physiological information on this time scale
Can be used on living systems to do real physiological experiments
Notes: 2

## Slide 3: The Advanced Photon Source

## Slide 4
SAXS Instrument on the BioCAT
Beamline 18ID at the APS

## Slide 5
Myofibrils and Sarcomeres
A myofibril consists of many 2-3 micron long sarcomeres laid end to end
In the light microscope, sarcomeres show a banding pattern (striations)
A-band, I band, Z-line, and M-line, H-zone
Underlying structure can be seen only at electron microscope level

## Slide 6
Sarcomeres
11-9
Sarcomere consists of actin containing thin filaments
Myosin containing thick filaments
I band contains only thin filaments
H-zone only thick
A-band both thick and thin

## Slide 7
Sarcomeres
11-9
Projections on the thick filament (crossbridges) interact with the thin filament and cause sarcomeres to shorten

## Slide 11
synchrotron X-ray source
evacuated flight tube
CCD
detector
muscle
bath
mirror
X-rays
1,0
1,1
actin
myosin



d
X-rays
A
B
C
diff.
AB=BC=d10 sin 
X-rays
F
2
D
2sin  = n/d
2sin  = D/(D2+F2)1/2
d10 = (n(D2+F2)1/2/D)/2
inter-thick filament spacing = d10*(2/3)
Using X-ray Diffraction to Measure Lattice Spacing

## Slide 12
Thin filaments near Z band
Thick and thin filaments overlapping in A-band
Cross-sections of a sarcomere showing 2-D crystalline structure
Thick filaments Only in H-zone

## Slide 13: Hexagonal Lattice
u
x
y
a

b

a

b


## Slide 14: Ewald Sphere
2 
1
h a*
k a*

For every lattice in real space there is a corresponding lattice in “recripocal” i.e. diffraction space. Distances between lattice points are proportional to 1/lattice dimensions in real space. The origin of the reciprocal lattice is at O. Lattice points (corresponding to diffraction spots one can observe) are indexed by Miller indices h and k
O

## Slide 15: End on view of hexagonal reciprocal lattice
This was taken by shining the X-ray beam down the axis of a muscle myofibril.(one crystallite)
Not the way we normally do it.

## Slide 16
X-rays
Fiber Cross-section
Diffraction
Complete Statistical rotation:
1,0 = 1,0 = 0,1 = 0,-1
1,1 = 1,1=1,1 = 1,-1
Myofibrils are at random orientations around the long axis of the muscle fiber

## Slide 17: Equatorial pattern from insect muscle
We are looking at projection of hexagonal lattice onto a plane. Insect muscle is highly ordered so you get lots of sharp spots along the equator.
Note that they vary in intensity
Equator

## Slide 18
undulator X-ray source
(electrons)
evacuated flight tube
(X-ray reflections)
CCD
detector
muscle
bath
mirror
X-rays
inverted
microscope
1,0
1,1
actin
myosin



d
X-rays
A
B
C
diff.
AB=BC=d10 sin 
X-rays
F
2
D
Experimental arrangement of the BioCAT undulator beam line for X-ray diffraction
2sin  = n/d
2sin  = D/(D2+F2)1/2
d = (n(D2+F2)1/2/D)/2
inter-thick filament spacing = d*(2/3)

## Slide 19: Calculating d10
Braggs Law
nλ = 2dsinθ
θ is the Bragg angle where 2 is the angle between the diffracted and incident beam
At small angles
Θ = D/2L so that
nλ = 2dD/2L
Or
d=nλL/D
So d, the spacing between the diffracting planes is inversely proportional to D, the distance from the origin of the diffraction pattern to a diffraction spot

## Slide 20: Hexagonal pattern selection rule
The distances from the center of the pattern to each of the outer reflections (Sh,k) are related to the distance from the center to the first strong 1,0 reflection, S10, by Sh,k = S10√(h2 + k2 + hk) where h and k are the Miller indices of each reflection. Notice that several combinations of h and k values will give rise to the same Sh,k meaning that X-ray reflections will superimpose.

## Slide 21: Estimating lattice disorder parameters from peak widths
The width of the Gaussian representing a given diffraction peak σh,k can be expressed as
σh,k = √(σc2+ σd2Shk + σs2Shk2) where Shk = √(h2 + k2 + hk). σc is the known width of the X-ray beam, σd is related to the amount of heterogeneity in inter-filament spacing among the myofibrils, and σs is related to the amount of paracrystalline (liquid-like) disorder of the myofilaments in the hexagonal lattice.
These are all interesting physiological paramaters

## Slide 22
Intensity of Equatorial Reflections as a Measure of Crossbridge Position
When crossbridges reach out and bind to actin there is an increase in the equatorial intensity ratio I11/I10
Notes: Changes in equatorial peak intensities upon activation . If we plot the intensity profiles of these reflections, we see just that in comparing resting to active muscle patterns. So on the right we see electron density patterns of resting muscle, with mass indicated by black spots and the unit cell defined by dotted lines. The big spots are myosin and the small spots are actin. In active muscle, the outline of the myosin spot becomes less well-defined and the actin spots increase in size dramatically. The intensity profiles of these patterns on the left clearly display the changes in the reflections, as the 1,0 intensity decreases and the 1,1 intensity increases.

## Slide 23
I1,1/I1,0 in mouse skeletal muscle
A linear relationship in equatorial intensity change to applied tension
Chart: Time(s)
| 0 | 0.05 | 0.1 | 0.15000000000000002 | 0.2 | 0.25 | 0.3 | 0.35 | 0.39999999999999997 | 0.44999999999999996 | 0.49999999999999994 | 0.54999999999999993 | 0.6 | 0.65 | 0.70000000000000007 | 0.75000000000000011 | 0.80000000000000016 | 0.8500000000000002 | 0.90000000000000024 | 0.95000000000000029 | 1.0000000000000002 | 1.0500000000000003 | 1.1000000000000003 | 1.1500000000000004 | 1.2000000000000004 | 1.2500000000000004 | 1.3000000000000005 | 1.3500000000000005 | 1.4000000000000006 | 1.4500000000000006 | 1.5000000000000007 | 1.5500000000000007 | 1.6000000000000008 | 1.6500000000000008 | 1.7000000000000008 | 1.7500000000000009 | 1.8000000000000009 | 1.850000000000001 | 1.900000000000001 | 1.9500000000000011 | 2.0000000000000009 | 2.0500000000000007 | 2.1000000000000005 | 2.1500000000000004 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.3499999999999996 | 2.3999999999999995 | 2.4499999999999993 | 2.4999999999999991 | 2.5499999999999989 | 2.5999999999999988 | 2.6499999999999986 | 2.6999999999999984 | 2.7499999999999982 | 2.799999999999998 | 2.8499999999999979
Tension | 1.0216 | 1.0627 | 0.9294 | 0.90116 | 0.92582 | 1.0893 | 1.0244 | 0.89757 | 0.98997 | 1.1195 | 9.9362 | 36.5168 | 58.2553 | 72.091 | 80.7695 | 86.3507 | 90.255 | 92.8668 | 94.7474 | 96.0921 | 97.1086 | 97.9636 | 98.3841 | 98.937 | 99.2032 | 99.4868 | 99.5479 | 99.7468 | 99.8346 | 99.9277 | 99.1338 | 92.6098 | 73.3864 | 44.615 | 27.0688 | 17.7657 | 12.1335 | 8.2246 | 5.2894 | 3.462 | 2.0465 | 1.2389 | 0.70776 | 0.51054 | 0.49283 | 0.39924 | 0.36741 | 0.14983 | 0.28866 | 0.099332 | 0.32264 | 0.37554 | 0.29536 | 0.22499 | 0.15366 | 0.31858 | 0.15821 | 0.43825
Consistent with studies on cardiac muscle: intensity ratio correlates well with tension especially during the early phase of contraction
(Matsubara Annu. Rev. Biophys. Bioeng., 9 (1980)
Notes: BB at various time to produce a wide range of force to get this whole intensity ratio change and tension curve. Looks linear
BB alter myosin behaviors which probably comprise the linear relationship.
What we plotted was the difference of intensity ratios between resting and plateau regions, what about the force arising phase. So we did a time-resolved experiment to look at this.
the intensity changes follows tension very well even though It wasn’t strictly linear.
And if only plot the curve upto 60% percent of maximum force, the relationship between I1,1/I1,0 and submaximum tension was linear.
Tension is proportional to the number of attached cross-bridges
Whether it is strictly linear or not, this makes the intensity ratio data more informative.

## Slide 24: Skeletal Muscle X-ray Diffraction at BioCAT
Weikang Ma, T. Irving
Illinois Institute of Technology, Chicago IL

## Slide 25
Mouse skeletal muscle XRD in BioCAT
DOI 10.1002/14356007.a12_319
Soleus
EDL
Notes: Early X-ray: insect IFM, and frog and rabbit psoas muscle
Why mouse skeletal muscle?
For every disease associate to any mutation in sarcomeric proeteins, a animal model can be generated. And mouse model was the most widely used.
Mouse soleus and EDL at 1cm long and 1mm wide which at the sweet spot for X-ray diffraction.

## Slide 26
Relaxing
Contracting
Equator
Meridian
Muscle X-ray pattern
Layer lines
Notes: Everything that is not on the meridian or the equator is called a layer line.

## Slide 27: Thin filament based reflections
5.9nm
5.1nm
Actin 2.73nm
2.73nm
Relaxing
Contracting
5.9nm
5.1nm
Notes: To really understand the diffraction patterns, you have to understand a radial projection.
Imagine a barber pole made of paper.
Take a pair of scissors and cut the paper tube vertically and flatten out the paper.
5.1nm pitch 5.9nm pitch 2.7nm axial displacement. And corresponding reflections

## Slide 28
Examples
Patient
Control
LH_Helix
Nebulin mutations leads to nemaline myopathy
Nebulin cKO mouse model (less nebulin expressed) –was used in this study
Shorter 5.9nm spacing was seen in human biopsy samples from NM Patient
Notes: Shorter 5.9 nm left handed helix pitch.
Animal model replicate the phenotypes of the corresponding human disease.

## Slide 29: Thin filament extensibility
Actin 2.73nm
Nebulin
Hypothesis:
WT
cKO
2.73nm
Nebulin stiffens the thin filament
Modified from Perz-Edwards, Unpublished
Relaxing
Contracting
Notes: The thin filament extensibility can be measured the by plotting the axial displacement changes against the applied tension

## Slide 30: Thin filament Extensibility
Thin filament
The 2.73nm relative spacing change as a function of isometric contraction
30.3 pN/(nm·μm)
10.0 pN/(nm·μm),
WT
2.73nm
cKO
Balazs Kiss, Eun-Jeong Lee, Weikang Ma, Frank W Li Paola Tonino, Srboljub M Mijailovich, Thomas C. Irving, Henk L. Granzier. Nebulin stiffens the thin filament and augments cross-bridge interaction in skeletal muscle (Proc Natl Acad Sci U S A. 115(41):10369-10374.
Notes: When we plot the thin filament extensibility from thin filament with and without nebulin, and the slope of the curve showed that the thin filament was three times stiffer with the presence of nebulin. In the meantime, the thick filament extensibility was measured as internal reference showed no difference between cKO and control.

## Slide 31: Myosin filament based reflections
M6 7.2nm
E. P. Debold. Biological machines: Molecular motor teamwork
MLL1 42.9nm
M3 14.3nm
MLL1: Helically ordered myosin heads
M3: Intensity primarily from myosin heads
M6: Intensity primarily from myosin backbone
Notes: The thick filament is a three strands quasi helix with an axial repeat at 42.9nm which will give the first myosin layer line and axial displacement at 14.3nm which will give the third order meridional reflection.
The intensities of M3 are primarily from the myosin heads, and the intensity of the higher orders namely M6 M9 and so on are primarily from the thick filament backbone.
The meridian reflections tell you about axial periodicities

## Slide 32: Bessel Functions and Layer lines
Transform of a cylinder

## Slide 33: Diffraction From a Discontinuous Helix
A set of points that are regularly spaced along a helical path
l=#residues*m+#turns*n
“Helical Selection Rule”
m indexes meridional reflections
n is the allowed orders of Bessel functions

## Slide 34: Diffraction from a helix: comparison
The main effect of shifting from a continuous to a discontinuous helix is to introduce new helix crosses with their origins displaced up and down the meridian by a distance 1/h

## Slide 35: Crystals of Helical Molecules

## Slide 36: Multi-Stranded (coiled coil) Helices
If N strands Only every Nth Layer -line allowed
Myosin Filaments are 3 stranded

## Slide 37: Myosin filament based reflections
M6
The layer line intensity distribution is on the basis of Bessel function
The distance between the first maximum layer is reversely related to the average myosin heads radius (Rm)
Rm
MLL1
MLL4
Notes: The characteristic X-ray diffraction pattern for helix structure is this X shape, and this was the X-ray diffraction pattern from DNA
The distance between the first maximum layer line reflection can be used to estimate the distribution of myosin heads along the thick filament
When muscle contracts, the helical structural was lost, and the myosin based layer line was replaced by actin based layer lines. So that the myosin layer line was proposed to be the indicator of myosin ON and OFF.

## Slide 38
SRX by Muscle X-ray Diffraction
There are two states of relaxed myosin heads: SRX and DRX
SRX was characterized structurally the heads are folded back on to its own coiled-coil S2 tail
Trivedi, et al 2018 Biophys Rev
If SRX is the only ordered state: MLL only from SRX heads
No changes in MLL spacing when more heads shift to SRX
Rm
Rm
Is DRX really disordered? Or there is another ordered RX
Smaller Rm when shifts more myosin heads to SRX
Notes: SRX state has been an interesting topic, and I think we found some ways to study it structurally.
It has been proposed that there are two states of relaxed myosin heads.
Structurally, the SRX was characterized as
Ordered thing diffracts, disordered thing scatters

## Slide 39
Rm became smaller with the presence of BB.
At least two ordered relaxed myosin states in skeletal muscle
IMLL increased with the presence of BB.
Increased MLL intensity and/or smaller average myosin heads radius could be indicators of SRX in X-ray diffraction under stable temperature.
Weikang Ma, Henry Gong and Thomas Irving. Myosin Head Configurations in Resting and Contracting Murine Skeletal Muscle. Int. J. Mol. Sci. 2018, 19(9), 2643; doi: 10.3390/ijms19092643
Notes: Blebbistatin, a small molecular myosin inhibitor, known to shifts myosin into SRX state
BTS, another small molecular myosin inhibitor was used for comparison purpose.
At least two ordered relaxed myosin state, at least in

## Slide 40: Structural Basis of the Frank-Starling “Law of the Heart”
Tom Irving1, Karen Hsu1,Younss Ait Mou2, Edward Allen2, Kelly Schoenfelt2 and Pieter P. de Tombe2
1 BioCAT, CSRRI, and Division of Biology, Illinois Institute of Technology
2 Dept. Physiology, Loyola University School of Medicine

## Slide 41
Activator [Ca2+]
Force Development
long SL
short SL
Ventricular Volume
Ventricular Pressure
SARCOMERE
VENTRICLE
Myofilament Length Dependent Activation (LDA) underlies the Frank-Starling’s Law of the Heart

## Slide 42: Myofilament Length Dependent Activation
Dobesh et al, AJP 2002
Long SL increases sensitivity to calcium

## Slide 43
How is the information concerning muscle length transmitted to the myofilaments?

## Slide 44
SHORT SL
LONG SL
Original idea:
Alterations in inter-filament spacing with changes in length underlie the increase in Ca2+-sensitivity with increases in length
Lattice Spacing Hypothesis now debunked – cannot explain all changes in calcium sensitivity in terms of changes in lattice spacing
de Tombe PP, et al, 2010 J Mol Cell Cardiol. 48(5):851-8.
Lattice Spacing Hypothesis

## Slide 45: Two Dimensional X-ray Diffraction: Sarcomere structure of Intact Twitching Cardiac Muscle

## Slide 46
Slack
Lmax
X-ray diffraction patterns from intact rat papillary muscle at slack and Lmax
Hypothesis: Increased calcium sensitivity is due to an outward movement of myosin heads with stretch

## Slide 47
Intensity of Equatorial Reflections as a Measure of Crossbridge Position
When crossbridges reach out and bind to actin there is an increase in the equatorial intensity ratio I11/I10
Notes: Changes in equatorial peak intensities upon activation . If we plot the intensity profiles of these reflections, we see just that in comparing resting to active muscle patterns. So on the right we see electron density patterns of resting muscle, with mass indicated by black spots and the unit cell defined by dotted lines. The big spots are myosin and the small spots are actin. In active muscle, the outline of the myosin spot becomes less well-defined and the actin spots increase in size dramatically. The intensity profiles of these patterns on the left clearly display the changes in the reflections, as the 1,0 intensity decreases and the 1,1 intensity increases.

## Slide 48
Our Hypothesis Predicts an Increase in I11/I10 At Longer SL
But a decrease is observed!
Heads appear to more associated with the thick filament backbone at long SL rather than with the thin filament
Farman et al. Am J Physiol Heart Circ Physiol. 201;300(6):H2155-60

## Slide 49: Layer Lines Allow Direct Measurement Radius of Heads
First myosin layer line (M1)
Position of maxima on layer lines inversely proportional to radius to the center of mass of myosin heads

## Slide 50: Myosin layer lines show inward radial motion of myosin heads with stretch
Lmax
Slack
Results show an inward movement of the myosin heads at long length consistent with I11/I10

## Slide 51
M3
M3
M3 reflection is a Measure of Orientation of Myosin Heads
M3 reflection intensity is a sensitive measure of myosin head orientation
Strongest when heads are perpendicular to thick filament backbone
M3 intensity in diastole well correlated with maximum systolic force (Farman et al 2011 AJPH 300:H2155)

## Slide 52
Conclusions
Myosin heads are closer to the thick filament backbone at long SL than short SL
Myosin heads are more perpendicular to the thick filament backbone at long SL than at short SL- better aligned with target zones on the thin filament?
  This tendency correlated with increases in calcium sensitivity
Still have not identified a length sensor – What else is going on in the 2D patterns?

## Slide 53
T3
M2
Slack (Red)
Lmax (Black)
Meridian of pattern gives information from structures along axes of filaments M2, M3,M6 -myosin, T3-troponin
M3
M6

## Slide 54
2nd order myosin reflection intensity
Stretch : increased M2 intensity (~2.8 fold; p < 0.05)
The m2 reflection is “forbidden” by helical symmetry
Must be a rearrangement of myosin heads between helically ordered and distorted regions on the surface of the thick filament (Malinchik & Lednev, 1992) so that more distortion at longer lengths
Head arrangement is different at longer SL!

## Slide 55
3rd order troponin reflection intensity
Stretch : Increased T3 intensity (~1.9 fold; p < 0.05)
Changes in the T3 reflection suggest changes in the orientation and position of the troponin complex when the thin filament is stretched similar to that seen when muscles contract (Maéda et al., 1992)

## Slide 56: Strain in the Thick Filament May be the Length Sensor
Thick filaments extend slightly (up to 0.3%) when sarcomeres stretched to longer lengths
The intensity of the m6 meridional reflection dominated by structures
In thick filament backbone

## Slide 57
Sarcomere stretch
Thick filament
thin filament
Z-line
F
Fr (F times sina)
Fl (F times cosa)
a
Titin Based Passive Tension as the Source of Thick Filament Strain

## Slide 58
passive F (mN/mm2)
SL (µm)
pCa50
active F (mN/mm2)
Use N2BA-G mutant rats with longer isoform of titin than WT
Much less passive force
No LDA
Much less peak active force
Greaser et al., J Mol Cell Cardiol. 44(6):983-91 2008
Testing the titin-based tension hypothesis:

## Slide 59
Lattice spacing (nm)
Wild-Type
mutant
short
long
short
long
I1,1 / I1,0 Ratio
Wild-Type
N2BA-G mutant
1,1
1,0

## Slide 60
WT
HM
WT
Slack
Lmax
Difference
M
M
A
M

## Slide 61
Wild-Type
Titin
mutant
M2
M3
M6
M4
Tn3
M5
M2 and Tn3 intensity changes seen in WT much reduced in mutant myocardium
Chart: WT
| M2lmax | M2slack | Tn3 lmax | Tn3 slack
 | 1053907.3053 | 545437.1061 | 343258.8727 | 170608.9721
Chart: Titin Mutant
| M2lmax | M2slack | Tn3 lmax | Tn3 slack
 | 173728.1111 | 146065.8222 | 70605.7333 | 57352.5556
M2
Tn3
M2
Tn3

## Slide 62
Conclusions
Changes in muscle length induce structural changes in both the thick filament and the troponin complex on the thin filaments.
Changes in the troponin complex structure in diastole could be the key part that underlies the molecular mechanism underlying length modulation of myofilament Ca2+ sensitivity.
Structural changes in the thick filament may modulate this mechanism

## Slide 63
Conclusions
Our results show that there must be communication between the thick and the thin filaments
There are significant numbers of bound crossbridges in cardiac muscle in diastole
Thick filaments are under strain due to titin-based passive tension when slack muscle is stretched

## Slide 64
Conclusions
Strain may be transmitted via crossbridges to the thin filaments
Strain in crossbridges somehow induces changes in the troponin complex
This may be the key step in length dependent activation

## Slide 66
Time-resolved X-ray Diffraction Studies of Drosophila Indirect Flight Muscle in vivo
Michael Dickinson
Mark Frye
(Caltech)
David Maughan (UVM)
Tom Irving (BioCAT/IIT)

## Slide 67
Important periodicities
38.7 nm
56 nm
Target Site
Lengthening
Shortening
Tn
19.3 nm
14.5 nm
d
7.2 nm

## Slide 68
Dickinson et al., 2005 Nature 433:330-4

## Slide 69
wing beat phase
0.5
1.0
0.0
1.5
2.0
% spacing change
0.25
0
-0.25
upstroke
downstroke
upstroke
downstroke
lengthen
shorten
lengthen
shorten
7.2 nm myosin periodicity
(thick filament length)
During each wingbeat a significant amount of strain energy is stored in stretching and releasing the thick filaments in the flight muscles
Two cycles of “movie”. Time between successive points ~ 600 µs
Dickinson et al.,2005 Nature;433:330-4

## Slide 70
wing beat phase
0.5
1.0
0.0
1.5
2.0
% intensity change
500
100
0
upstroke
downstroke
upstroke
downstroke
lengthen
shorten
lengthen
shorten
400
300
200
600
19.3 nm first row line spot intensity
(crossbridge attachment)
Crossbridges are recruited to actin binding sites while the flight muscle is being stretched.
During the downstroke, force producing crossbridges cycle and then detach abruptly
Suggests strain dependent mechanisms for both crossbridge recruitment and detachment
Two cycles of “movie”. Time between successive points ~ 600 µs
Dickinson et al.,2005 Nature;433:330-4

## Slide 71
Robert J. Perz-Edwards, Thomas C. Irving, Bruce A. J. Baumann, David Gore, Daniel C. Hutchinson, Uroš Kržič, Rebecca L. Porter, Andrew B. Ward, Michael K. Reedy. “X-ray diffraction evidence for myosin-troponin connections and tropomyosin movement during stretch activation of insect flight muscle" PNAS, 108:120-5. 2011
X-ray diffraction evidence for tropomyosin movement during stretch activation of insect flight muscle

## Slide 72
Visualization of Troponin/Tropomyosin system during oscillatory contraction of Insect Flight Muscle
X-ray Movies During Oscillatory Contraction
Perz-Edwards et al., 2011 PNAS 108:120-5

## Slide 73
Active
Relaxed

## Slide 74
NET
Str-ACT Force
PHASING
INTENSITY of TROPOMYOSIN Layer Line
Str-ACT shows strong single peak; leading edge ahead of NET force rise.
TROPOMYOSIN Layer Line
Notes: 74

## Slide 75
In vertebrate striated muscle, high calcium binds troponin causing azimuthal shift of tropomyosin, exposing the myosin binding sites on actin
Difference in stretch activation is that mechanical strain delivered by a small number of bound crossbridges, perhaps special “troponin bridges” allows tropomyosin to move
.
Stretch Activation Works by the Familiar “Steric Blocking” Mechanism

## Slide 77: Equatorial Intensities
If crossbridges move away from the thick filament backbone towards the thin filament
Mass leaves the 1,0 plane and joins 2,0
I2,0/I1,0 goes up

## Slide 78: Equatorial Intensities
UseI2,0/I1,0 as a measure of degree of association crossbridges with thin filament
In vertebrate muscle use I1,1/I1,0 instead